## Slide 1
AC/GEN-SET
SmartCharge-12000 PFC
Control Interface
BMM
Accumulator

## Slide 2: Chargers
EV8.3.1 Only chargers presented and sealed at Electrical Tech Inspection are allowed. All connections of the charger(s) must be isolated and covered. No open connections are allowed.
EV8.3.2 All chargers must either be accredited to a recognized standard e.g. CE or where built by the team they must be built to high standards and conform with all electrical requirements for the vehicle tractive system, for example EV4.1, EV4.3 and EV4.6 as appropriate.
EV8.3.3 The charger connector must incorporate an interlock such that neither side of the connector become live unless it is correctly connected to the accumulator.
EV8.3.4 HV charging leads must be orange
EV8.3.5 When charging, the AMS must be live and must be able to turn off the charger in the event that a fault is detected.
EV8.3.6 The charger must include a push type emergency stop button which has a minimum diameter of 25mm and must be clearly labeled.
EV8.3.7 When charging the accumulator, the IMD must be active and must be able to shut down the charger. In the case that the accumulator is charged outside of the vehicle, either the charger must incorporate an active IMD or an active IMD must be within the accumulator.

## Slide 3: EV 4.1V Separation of Traction System and Grounded Low Voltage System
EV4.1.1 The layout of electrical devices designed by the team must be documented accurately in the ESF.
EV4.1.2 There must be no connection between the frame of the vehicle (or any other conductive surface that might be inadvertently touched by a crew member or spectator), and any part of any tractive system circuits.
EV4.1.3 Tractive system and GLV circuits must be physically segregated such that they are not run through the
same conduit or connector, except for interlock circuit connections.
EV4.1.4 GLV systems must not be included in the accumulator container except for required purposes. Exceptions include the AIRs, HV DC/CD converters, the AMS and the IMD. All GLV systems in the accumulator container must have galvanic isolation for all connections to the outside of the accumulator container. Any LV wiring within the accumulator container, and where appropriate its galvanic isolation must be described within the ESF.
EV4.1.5 Where both tractive system and GLV are present within an enclosure, they must be separated by insulating barriers made of moisture resistant, UL recognized or equivalent insulating materials rated for 150 C or higher (e.g. Nomex based electrical insulation), or maintain the following spacing
through air, or over a surface (similar to those defined in UL1741):
• U < 100VDC 10 mm (0.4 inch)
• 100VDC < U < 200VDC 20 mm (0.75 inch)
• U > 200VDC 30 mm (1.2 inch)
EV4.1.6 Spacing must be clearly defined. Components and cables capable of movement must be positively restrained to maintain spacing.
EV4.1.7 If tractive system and GLV are on the same circuit board, they must be on separate, clearly defined areas of the board. Furthermore the tractive system and GLV areas have to be clearly marked on the PCB. NOTE: The following spacing is related to the spacing between traces / board areas. If integrated circuits are used such as opto-couplers which are rated for the respective maximum tractive system voltage, but do not fulfill the required spacing, then they may still be used and the given spacing do not apply. Required spacing are as follows:
EV4.1.8 Teams must be prepared to demonstrate spacing on team-built equipment. Information on this must be included in the electrical system form (EV9.1). For inaccessible circuitry, spare boards or appropriate photographs must be available for inspection.
EV4.1.9 All connections to external devices such as laptops from a tractive system component must include galvanic isolation.
EV4.2 Positioning of tractive system parts
EV4.2.1 All parts belonging to the tractive system including cables and wiring must be contained within the envelope of any part of the frame which is made from any regulated tubing defined in T3.4 and/or an additional envelope of tubing which meets the minimum specification defined in T3.4 or equivalent, such that they are protected against being damaged in case of a crash or roll-over situation.
EV4.2.2 If tractive system parts are mounted in a position where damage could occur from a rear or side impact (below 350mm from the ground), for example motors at the rear of the car, they have to be protected by a fully triangulated structure with tubes of a minimum outer diameter of 25.4mm and a minimum wall thickness of 1.25mm or equivalent – see T3.4.
EV4.2.3 Outboard wheel motors are allowed where the motor is outside of the frame but only if an interlock is added such that the shutdown circuit, EV5.1, is activated and the AIRs are opened if the wheel assembly is damaged or knocked off the car.
EV4.2.4 In side or front view no part of the tractive-system can project below the lower surface of the frame or the monocoque, whichever is applicable.
EV4.2.5 Additional regulations apply for accumulators, see EV3.4.

## Slide 4: EV4.3 Grounding
EV4.3.1 All electrically conductive parts of the vehicle (e.g. parts made of steel, (anodized) aluminum, any other metal parts, etc.) which are within 100mm of any tractive system or GLV component , and any driver harness mounting points, seat mounting points and driver controls must have a resistance below 300 mOhms (measured with a current of 1A) to GLV system ground.
EV4.3.2 All parts of the vehicle which may become electrically conductive (e.g. completely coated metal parts, carbon fiber parts, etc.) which are within 100mm of any tractive system or GLV component, must have a resistance below 5 Ohm to GLV system ground.
EV4.3.3 Electrical conductivity of any part may be tested by checking any point which is likely to be conductive, for example the driver's harness attachment bolt, but where no convenient conductive point is available then an area of coating may be removed. NOTE: Carbon fiber parts may need special measures such as using copper mesh or similar to keep the ground resistance below 5 Ohms.

## Slide 5: EV4.6 Tractive System Enclosures
EV4.6.1 Every housing or enclosure containing parts of the tractive system, except motor housings, must be labeled with (a) reasonably sized sticker(s) with a red or black lightning bolt on yellow background or red lightning bolt on white background. The sticker must also contain the text “High Voltage” or something similar if the voltage is more than 60V DC or 25VAC.
EV4.6.2 If the housing material is electrically conductive or possibly electrically conductive, it must have a low-resistance connection to GLV system ground, see EV4.3.